## Slide 1: BGP Protocol & Configuration
AfNOG

## Slide 2: Border Gateway Protocol (BGP4)
Case Study 1, Exercise 1: Single upstream
Part 6: BGP Protocol Basics
Part 7: BGP Protocol - more detail
Case Study 2, Exercise 2: Local peer
Part 8: Routing Policy and Filtering
Exercise 3: Filtering on AS-path
Exercise 4: Filtering on prefix-list
Part 9: More detail than you want
Exercise 5: Interior BGP
Part 10: BGP and Network Design

## Slide 3: BGP Part 6
BGP Protocol Basics
Terminology
General Operation
Interior/Exterior BGP

## Slide 4: BGP Protocol Basics
Routing Protocol used between ASes
  If you aren’t connected to multiple ASes you don’t need BGP
Runs over TCP
AS 100
AS 101
AS 102
E
B
D
A
C
Peering

## Slide 5: BGP Protocol Basics
Uses Incremental updates
  sends one copy of the RIB at the beginning, then sends changes as they happen
Path Vector protocol
  keeps track of the AS path of routing information
Many options for policy enforcement

## Slide 6: Terminology
Neighbour
  Configured BGP peer
NLRI/Prefix
  NLRI – network layer reachability information
  Reachability information for an IP address & mask
Router-ID
  32 bit integer to uniquely identify router
  Comes from Loopback or Highest IP address configured on the router
Route/Path
  NLRI advertised by a neighbour

## Slide 7: Terminology
Transit – carrying network traffic across a network, usually for a fee
Peering – exchanging routing information and traffic
  your customers and your peers’ customers network information only.
  not your peers’ peers; not your peers’ providers.
Peering also has another meaning:
  BGP neighbour, whether or not transit is provided
Default – where to send traffic when there is no explicit route in the routing table

## Slide 8: BGP Basics …
Each AS originates a set of NLRI (routing announcements)
NLRI is exchanged between BGP peers
Can have multiple paths for a given prefix
BGP picks the best path and installs in the IP forwarding table
Policies applied (through attributes) influences BGP path selection

## Slide 9: Interior BGP vs. Exterior BGP
Interior BGP (iBGP)
  Between routers in the same AS
  Often between routers that are far apart
  Should be a full mesh: every iBGP router talks to all other iBGP routers in the same AS
Exterior BGP (eBGP)
  Between routers in different ASes
  Almost always between directly-connected routers (ethernet, serial line, etc.)

## Slide 10: BGP Peers
AS 100
AS 101
AS 102
A
C
E
B
D
100.100.8.0/24
100.100.16.0/24
100.100.32.0/24
BGP Peers exchange Update messages containing Network Layer Reachability Information (NLRI)
BGP Update
Messages

## Slide 11: BGP Peers – External (eBGP)
BGP speakers are called peers
eBGP TCP/IP
Peer Connection
Peers in different AS’s are called External Peers
Note: eBGP Peers normally should be directly connected.
AS 100
AS 101
AS 102
A
C
E
B
D
100.100.8.0/24
100.100.16.0/24
100.100.32.0/24

## Slide 12: BGP Peers – Internal (iBGP)
AS 100
AS 101
AS 102
A
C
BGP speakers are called peers
Peers in the same AS are called Internal Peers
Note: iBGP Peers don’t have to be directly connected.
E
B
D
100.100.8.0/24
100.100.16.0/24
100.100.32.0/24
iBGP TCP/IP
Peer Connection

## Slide 13: Configuring eBGP peers
BGP peering sessions are established using the BGP “neighbor” command
  eBGP is configured when AS numbers are different
interface Serial 0
ip address 110.110.10.2 255.255.255.252
router bgp 100
network 100.100.8.0 mask 255.255.255.0
neighbor 110.110.10.1 remote-as 101
interface Serial 0
ip address 110.110.10.1 255.255.255.252
router bgp 101
network 100.100.16.0 mask 255.255.255.0
neighbor 110.110.10.2 remote-as 100
110.110.10.0/30
B
C
D
A
AS 100
AS 101
.2
100.100.8.0/30
100.100.16.0/30
.2
.1
.2
.1
.1

## Slide 14: Configuring iBGP peers
BGP peering sessions are established using the BGP “neighbor” command
  iBGP is configured when AS numbers are the same
AS 100
AS 101
110.110.10.0/30
.2
interface Serial 1
ip address 100.100.16.2 255.255.255.252
router bgp 101
network 100.100.16.0 mask 255.255.255.0
neighbor 100.100.16.1 remote-as 101
B
interface Serial 1
ip address 100.100.16.1 255.255.255.252
router bgp 101
network 100.100.16.0 mask 255.255.255.0
neighbor 100.100.16.2 remote-as 101
C
D
100.100.8.0/30
100.100.16.0/30
A
.2
.1
.2
.1
.1

## Slide 15: Configuring iBGP peers: Full mesh
Each iBGP speaker must peer with every other iBGP speaker in the AS
iBGP TCP/IP
Peer Connection
AS 100
A
B
C

## Slide 16: Configuring iBGP peers: Full mesh
Each iBGP speaker must peer with every other iBGP speaker in the AS
This can be a pain if there are many routers, but there are ways to deal with it (route reflectors)
iBGP TCP/IP
Peer Connection
A
E
D
C
B

## Slide 17: Configuring iBGP peers: Loopback interface
iBGP TCP/IP
Peer Connection
AS 100
A
B
C
105.10.7.1
105.10.7.2
105.10.7.3
Loopback interfaces are normally used as the iBGP peer connection end-points

## Slide 18: Configuring iBGP peers
AS 100
A
B
C
105.10.7.1
105.10.7.2
105.10.7.3
interface loopback 0
ip address 105.10.7.1 255.255.255.255
router bgp 100
network 105.10.7.0 mask 255.255.255.0
neighbor 105.10.7.2 remote-as 100
neighbor 105.10.7.2 update-source loopback0
neighbor 105.10.7.3 remote-as 100
neighbor 105.10.7.3 update-source loopback0

## Slide 19: Configuring iBGP peers
AS 100
A
B
C
105.10.7.1
105.10.7.2
105.10.7.3
interface loopback 0
ip address 105.10.7.2 255.255.255.255
router bgp 100
network 105.10.7.0 mask 255.255.255.0
neighbor 105.10.7.1 remote-as 100
neighbor 105.10.7.1 update-source loopback0
neighbor 105.10.7.3 remote-as 100
neighbor 105.10.7.3 update-source loopback0
iBGP TCP/IP
Peer Connection

## Slide 20: Configuring iBGP peers
AS 100
A
B
C
105.10.7.1
105.10.7.2
105.10.7.3
interface loopback 0
ip address 105.10.7.3 255.255.255.255
router bgp 100
network 105.10.7.0 mask 255.255.255.0
neighbor 105.10.7.1 remote-as 100
neighbor 105.10.7.1 update-source loopback0
neighbor 105.10.7.2 remote-as 100
neighbor 105.10.7.2 update-source loopback0