## Slide 1: BGP Protocol & Configuration
AfNOG

## Slide 2: BGP Part 8
Routing Policy
Filtering

## Slide 3: Terminology: “Policy”
Where do you want your traffic to go?
  It is difficult to get what you want, but you can try
Control of how you accept and send routing updates to neighbors
  prefer cheaper connections, load-sharing, etc.
Accepting routes from some ISPs and not others
Sending some routes to some ISPs and not others
Preferring routes from some ISPs over others

## Slide 4: Routing Policy
Why?
  To steer traffic through preferred paths
  Inbound/Outbound prefix filtering
  To enforce Customer-ISP agreements
How?
  AS based route filtering – filter list
  Prefix based route filtering – prefix list
  BGP attribute modification – route maps
  Complex route filtering – route maps

## Slide 5: Filter list rules: Regular Expressions
Regular Expression is a pattern to match against an input string
Used to match against AS-path attribute
ex: ^3561_.*_100_.*_1$
Flexible enough to generate complex filter list rules

## Slide 6: Regular expressions (cisco specific)
^ matches start
$ matches end
_ matches start, or end, or space (boundary between words or numbers)
.* matches anything (0 or more characters)
.+ matches anything (1 or more characters)
[0-9] matches any number between 0 and 9
^$ matches the local AS (AS path is empty)
There are many more possibilities

## Slide 7: Filter list – using as-path access list
Listen to routes originated by AS 3561. Implicit deny everything else inbound.
Don’t announce routes originated by AS 35, but announce everything else (outbound).
ip as-path access-list 1 permit _3561$
ip as-path access-list 2 deny _35$
ip as-path access-list 2 permit .*
router bgp 100
neighbor 171.69.233.33 remote-as 33
neighbor 171.69.233.33 filter-list 1 in
neighbor 171.69.233.33 filter-list 2 out

## Slide 8: AS-Path acts on a Network
as-path access-lists work for both IPv4 and IPv6 because it performs a match for an ASN.
That means that it works equally well for IPv4 and IPv6.

## Slide 9: Policy Control – Prefix Lists
Per neighbor prefix filter
  incremental configuration
High performance access list
Inbound or Outbound
Based upon network numbers (using CIDR address/mask format)
First relevant “allow” or “deny” rule wins
Implicit Deny All as last entry in list

## Slide 10: Prefix Lists – Examples
Deny default route ip prefix-list Example deny 0.0.0.0/0
Permit the prefix 35.0.0.0/8 ip prefix-list Example permit 35.0.0.0/8
Deny the prefix 172.16.0.0/12, and all more-specific routes ip prefix-list Example deny 172.16.0.0/12 ge 12
  “ge 12” means “prefix length /12 or longer”. For example, 172.17.0.0/16 will also be denied.
In 192.0.0.0/8, allow any /24 or shorter prefixes ip prefix-list Example permit 192.0.0.0/8 le 24
  This will not allow any /25, /26, /27, /28, /29, /30, /31 or /32

## Slide 11: Prefix Lists – More Examples
In 192/8 deny /25 and above
  ip prefix-list Example deny 192.0.0.0/8 ge 25
  This denies all prefix sizes /25, /26, /27, /28, /29, /30, /31 and /32 in the address block 192.0.0.0/8
  It has the same effect as the previous example
In 192/8 permit prefixes between /12 and /20
ip prefix-list Example permit 192.0.0.0/8 ge 12 le 20
  This denies all prefix sizes /8, /9, /10, /11, /21, /22 and higher in the address block 193.0.0.0/8
Permit all prefixes
  ip prefix-list Example permit 0.0.0.0/0 le 32

## Slide 12: Policy Control Using Prefix Lists
Example Configuration
router bgp 200
network 215.7.0.0
neighbor 220.200.1.1 remote-as 210
neighbor 220.200.1.1 prefix-list PEER-IN in
neighbor 220.200.1.1 prefix-list PEER-OUT out
!
ip prefix-list PEER-IN deny 215.7.0.0/16 le 32
ip prefix-list PEER-IN permit 0.0.0.0/0 le 32
ip prefix-list PEER-OUT permit 215.7.0.0/16
ip prefix-list PEER-OUT deny 0.0.0.0/0 le 32
  Accept everything except our network (and subnets) from our peer
  Send only our network to our peer

## Slide 13: Prefix-lists in IPv6
Prefix-lists in IPv6 work the same way as they do in IPv4
  Caveat: ipv6 prefix-lists cannot be used for ipv4 neighbours - and vice-versa
  Syntax is very similar, for example:
ip prefix-list ipv4-ebgp permit 0.0.0.0/0 le 32
ip prefix-list v4out permit 172.16.0.0/16
!
ipv6 prefix-list ipv6-ebgp permit ::/0 le 128
ipv6 prefix-list v6out permit 2001:db8::/32

## Slide 14: Policy Control – Route Maps
A route-map is like a “program” for Cisco IOS
Has “line” numbers, like programs
Each line is a separate condition/action
Concept is basically:
if match then do expression and exit
else
if match then do expression and exit
else etc

## Slide 15: Route-map match & set clauses
Match Clauses
  AS-path
  Community
  IP address
Set Clauses
  AS-path prepend
  Community
  Local-Preference
  MED
  Origin
  Weight
  Others...

## Slide 16: Route Map: Example One
router bgp 300
neighbor 2.2.2.2 remote-as 100
neighbor 2.2.2.2 route-map SETCOMMUNITY out
!
route-map SETCOMMUNITY permit 10
match ip address 1
match community 1
set community 300:100
!
access-list 1 permit 35.0.0.0
ip community-list 1 permit 100:200
! When you are sending information OUT to neighbor
! 2.2.2.2, then: if the prefix/mask matches
! access-list 1, and if the community matches
! community-list 1, then:
! do “set community 300:100”

## Slide 17: Route Map: Example Two
Example Configuration as AS PATH prepend
router bgp 300
network 215.7.0.0
neighbor 2.2.2.2 remote-as 100
neighbor 2.2.2.2 route-map SETPATH out
!
route-map SETPATH permit 10
set as-path prepend 300 300
Use your own AS number for prepending
  Otherwise BGP loop detection will cause disconnects

## Slide 18: BGP Exercise 3
Filtering peer routes using AS-path regular expression

## Slide 19: Exercise 3: Filtering peer routes using AS-path
Create “ip as-path access-list <number>” to match your own routes
  ip as-path access-list 2 permit ^$
Apply the outbound filter to both upstreams
  “neighbor <upstream-addr> filter-list 2 out”

## Slide 20: Exercise 3: What you should see
From upstream: all routes
To upstream: your routes, no transit

## Slide 21: Exercise 3: Did it work?
IPv4 show commands:
  “show ip route” – your forwarding table
  “show ip bgp” – your BGP table
  “show ip bgp neighbor xxx received-routes” – from your neighbour before filtering
  “show ip bgp neighbor xxx routes” – from neighbour, after filtering
  “show ip bgp neighbor advertised-routes” – to neighbour, after filtering

## Slide 22: Exercise 3: Filtering peer routes using AS-path ---- xxx to remove?
Create “ip as-path access-list <number>” to match your own (internal) routes
  ip as-path access-list 1 permit ^1$
Create “ip as-path access-list <number>” to match your own routes
  ip as-path access-list 2 permit ^$
Apply the filters to both IPv4 and IPv6 peers:
  “neighbor <address> filter-list 1 in”
  “neighbor <address> filter-list 2 out”
  As-path filters are protocol independent, so the same filter can be applied to both IPv4 and IPv6 peers!
Apply the outbound filter to the AS100 upstream
  “neighbor <upstream-addr> filter-list 2 out”

## Slide 23: Exercise 3: Did it work?
IPv6 show commands:
  “show ipv6 route” – your forwarding table
  “show bgp ipv6” – your BGP table
  “show bgp ipv6 neighbor xxx received-routes” – from your neighbour before filtering
  “show bgp ipv6 neighbor xxx routes” – from neighbour, after filtering
  “show bgp ipv6 neighbor advertised-routes” – to neighbour, after filtering

## Slide 24: BGP Exercise 4
Filtering peer routes using prefix-lists

## Slide 25: Exercise 4: Filtering peer routes using prefix-list (IPv4)
Create “ip prefix-list my-routes” to match your own routes
Create “ip prefix-list peer-as-xxx” to match your peer’s routes
Apply the filters to your peers
  “neighbor xxx prefix-list my-routes out”
  “neighbor xxx prefix-list peer-as-xxx in”
Apply the outbound filter to your upstream provider
  “neighbor xxx prefix-list my-routes out”

## Slide 26: Exercise 4: Filtering peer routes using prefix-list (IPv6)
Create “ipv6 prefix-list myv6-routes” to match your own routes
Create “ipv6 prefix-list peer-as-xxx-v6” to match your peer’s routes
Apply the filters to your IPv6 peers
  “neighbor xxx prefix-list myv6-routes out”
  “neighbor xxx prefix-list peer-as-xxx-v6 in”
Apply the outbound filter to your upstream provider
  “neighbor xxx prefix-list myv6-routes out”

## Slide 27: Exercise 4: What you should see
From peers: only their routes, no transit
To peers: only your routes, no transit
From upstream: all routes
To upstream: only your routes, no transit
We still trust the upstream provider too much. Should filter it too!
  See “ip prefix-list sanity-filter” and “ipv6 prefix-list v6sanity-filter” in the cheat sheet

## Slide 28: Exercise 4: Did it work?
IPv4 show commands:
  “show ip route” – your forwarding table
  “show ip bgp” – your BGP table
  “show ip bgp neighbor xxx received-routes” – from your neighbour before filtering
  “show ip bgp neighbor xxx routes” – from neighbour, after filtering
  “show ip bgp neighbor advertised-routes” – to neighbour, after filtering

## Slide 29: Exercise 4: Did it work?
IPv6 show commands:
  “show ipv6 route” – your routing table
  “show bgp ipv6” – your BGP table
  “show bgp ipv6 neighbor xxx received-routes” – from your neighbour before filtering
  “show bgp ipv6 neighbor xxx routes” – from neighbour, after filtering
  “show bgp ipv6 neighbor advertised-routes” – to neighbour, after filtering