## Slide 1: BGP Protocol & Configuration
AfNOG

## Slide 2: Border Gateway Protocol (BGP4)
Case Study 1, Exercise 1: Single upstream
Part 6: BGP Protocol Basics
Part 7: BGP Protocol - more detail
Case Study 2, Exercise 2: Local peer
Part 8: Routing Policy and Filtering
Exercise 3: Filtering on AS-path
Exercise 4: Filtering on prefix-list
Part 9: More detail than you want
Exercise 5: Interior BGP
Part 10: BGP and Network Design

## Slide 3: BGP Part 10
BGP and Network Design

## Slide 4: Stub AS
Enterprise network, or small ISP
Typically no need for BGP
Point default towards the ISP
ISP advertises the stub network to Internet
Policy confined within ISP policy

## Slide 5: Stub AS
AS 100
AS 101
B
A
Provider
Customer

## Slide 6: Multihomed AS
Enterprise network or small ISP
Only border routers speak BGP
  And others on direct path between them
iBGP only between border routers
Rest of network either has:
  exterior routes redistributed in a controlled fashion into IGP…
  …or use defaults (much preferred!)

## Slide 7: Multi-homed AS
More details on multihoming coming up...
AS 100
AS 200
AS 300
D
C
B
A
provider
provider
customer
eBGP
iBGP

## Slide 8: Service Provider Network
iBGP used to carry exterior routes
  No redistribution into IGP
IGP used to track topology inside your network
Full iBGP mesh required
  Every router in ISP backbone should talk iBGP to every other router
  This has scaling problems, and solutions (e.g. route reflectors)

## Slide 9: Common Service Provider Network
AS 100
AS 200
AS 400
AS 300
F
E
D
G
H
C
B
A
provider
iBGP

## Slide 10: Load-sharing – single path
Router A:
interface loopback 0
ip address 20.200.0.1 255.255.255.255
!
router bgp 100
neighbor 10.200.0.2 remote-as 200
neighbor 10.200.0.2 update-source loopback0
neighbor 10.200.0.2 ebgp-multihop 2
!
ip route 10.200.0.2 255.255.255.255 <DMZ-link1>
ip route 10.200.0.2 255.255.255.255 <DMZ-link2>
AS100
AS200
Loopback 0
10.200.0.2
Loopback 0
20.200.0.1
A

## Slide 11: Load-sharing – multiple paths from the same AS
Note: A still only advertises one “best” path to iBGP peers
Router A:
router bgp 100
neighbor 10.200.0.1 remote-as 200
neighbor 10.300.0.1 remote-as 200
maximum-paths 2
100
200
A

## Slide 12: Redundancy – Multi-homing
Reliable connection to Internet
3 common cases of multi-homing
  default from all providers
  customer + default from all providers
  full routes from all providers
Address Space
  comes from upstream providers, or
  allocated directly from registries

## Slide 13: Default from all providers
Low memory/CPU solution
Provider sends BGP default
  provider is selected based on IGP metric
Inbound traffic decided by providers’ policy
  Can influence using outbound policy, example: AS-path prepend

## Slide 14: Default from all providers
AS 400
Provider
AS 200
Provider
AS 300
E
B
C
A
D
Receive default from upstreams
Receive default from upstreams

## Slide 15: Customer prefixes plus default from all providers
Medium memory and CPU solution
Granular routing for customer routes, default for the rest
  Route directly to customers as those have specific policies
Inbound traffic decided by providers’ policies
  Can influence using outbound policy

## Slide 16: Customer routes from all providers
C chooses shortest AS path
AS 400
Provider
AS 200
Customer
AS 100 160.10.0.0/16
Provider
AS 300
E
B
C
A
D

## Slide 17: Full routes from all providers
More memory/CPU
Fine grained routing control
Usually transit ASes take full routes
Usually pervasive BGP

## Slide 18: Full routes from all providers
C chooses shortest AS path
AS 400
AS 200
AS 100
AS 300
E
B
C
A
D
AS 500

## Slide 19: Best Practices IGP in Backbone
IGP connects your backbone together, not your clients’ routes
  Clients’ routes go into iBGP
  Hosting and service LANs go into iBGP
  Dial/Broadband/Wireless pools go into iBGP
IGP must converge quickly
  The fewer prefixes in the IGP the better
IGP should carry netmask information – OSPF, IS-IS, EIGRP

## Slide 20: Best Practices iBGP in Backbone
iBGP runs between all routers in backbone
Configuration essentials:
  Runs between loopbacks
  Next-hop-self
  Send-community
  Passwords
  All non-infrastructure prefixes go here

## Slide 21: Best Practices... Connecting to a customer
Static routes
  You control directly
  No route flaps
Shared routing protocol or leaking
  Strongly discouraged
  You must filter your customers info
  Route flaps
BGP for multi-homed customers
  Private AS for those who multihome on to your backbone
  Public AS for the rest

## Slide 22: Best Practices... Connecting to other ISPs
Advertise only what you serve
Take back as little as you can
Take the shortest exit
Aggregate your routes!!
  Consult RIPE-399 document for recommendations:
  http://www.ripe.net/docs/ripe-399.html
FILTER! FILTER! FILTER!

## Slide 23: Summary
We have learned about:
  BGP Protocol Basics
  Routing Policy and Filtering
  BGP Best Path Computation
  Typical BGP topologies
  Routing Policy
  BGP Network Design
  Redundancy/Load sharing
  Some best practices