## Slide 1: BGP Protocol & Configuration
AfNOG

## Slide 2: Border Gateway Protocol (BGP4)
Case Study 1, Exercise 1: Single upstream
Part 6: BGP Protocol Basics
Part 7: BGP Protocol - more detail
Case Study 2, Exercise 2: Local peer
Part 8: Routing Policy and Filtering
Exercise 3: Filtering on AS-path
Exercise 4: Filtering on prefix-list
Part 9: More detail than you want
Part 10: BGP and Network Design

## Slide 3: BGP Part 7
BGP Protocol – A little more detail

## Slide 4: BGP Updates — NLRI
Network Layer Reachability Information
Used to advertise feasible routes
Composed of:
  Network Prefix
  Mask Length
  Attributes of the path between you and the destination

## Slide 5: BGP Updates — Attributes
Used to convey information associated with NLRI
  AS path
  Next hop
  Local preference
  Multi-Exit Discriminator (MED)
  Community
  Origin
  Aggregator

## Slide 6: AS-Path Attribute
Sequence of ASes a route has traversed
Loop detection
Apply policy
AS 100
AS 300
AS 200
AS 500
AS 400
170.10.0.0/16
180.10.0.0/16
150.10.0.0/16
Network Path
180.10.0.0/16 300 200 100
170.10.0.0/16 300 200
150.10.0.0/16 300 400
Network Path
180.10.0.0/16 300 200 100
170.10.0.0/16 300 200

## Slide 7: AS-Path (with 16 and 32-bit ASNs)
Internet with 16-bit and 32-bit ASNs
Old software sees 23456 instead of actual ASN
AS-PATH length maintained
AS 80000
AS 300
AS 70000
AS 90000
AS 400
170.10.0.0/16
180.10.0.0/16
150.10.0.0/16
180.10.0.0/16 300 70000 80000
170.10.0.0/16 300 70000
150.10.0.0/16 300 400
180.10.0.0/16 300 23456 23456
170.10.0.0/16 300 23456

## Slide 8: Next Hop Attribute
160.10.0.0/16
150.10.0.0/16
192.10.1.0/30
.2
AS 100
AS 200
Network Next-Hop Path
160.10.0.0/16 192.20.2.1 100
C
.1
B
A
.1
.2
192.20.2.0/30
AS 300
E
D
140.10.0.0/16
BGP Update
Messages
Next hop to reach a network
Usually a local network is the next hop in eBGP session

## Slide 9: Next Hop Attribute
Next hop to reach a network
Usually a local network is the next hop in eBGP session
Next Hop updated between eBGP Peers
160.10.0.0/16
150.10.0.0/16
192.10.1.0/30
.2
AS 100
AS 200
C
.1
B
A
.1
.2
192.20.2.0/30
AS 300
E
D
140.10.0.0/16
BGP Update
Messages
Network Next-Hop Path
150.10.0.0/16 192.10.1.1 200
160.10.0.0/16 192.10.1.1 200 100

## Slide 10: Next Hop Attribute
Next hop not changed between iBGP peers
160.10.0.0/16
150.10.0.0/16
192.10.1.0/30
.2
AS 100
AS 200
C
.1
B
.1
.2
192.20.2.0/30
AS 300
E
D
140.10.0.0/16
BGP Update
Messages
Network Next-Hop Path
150.10.0.0/16 192.10.1.1 200
160.10.0.0/16 192.10.1.1 200 100
A

## Slide 11: Next Hop Attribute (more)
IGP is used to carry route to next hops
Recursive route look-up
  BGP looks into IGP to find out next hop information
  BGP is not permitted to use a BGP route as the next hop
Isolates BGP from actual physical topology
Allows IGP to make intelligent forwarding decision

## Slide 12: Next Hop Best Practice
Cisco IOS default is for external next-hop to be propagated unchanged to iBGP peers
  This means that IGP has to carry external next-hops
  Forgetting means external network is invisible
  With many eBGP peers, it is extra load on IGP
ISP best practice is to change external next-hop to be that of the local router
neighbor x.x.x.x next-hop-self

## Slide 13: Community Attribute
32-bit number
Conventionally written as two 16-bit numbers separated by colon
  First half is usually an AS number
  ISP determines the meaning (if any) of the second half
Carried in BGP protocol messages
  Used by administratively-defined filters
  Not directly used by BGP protocol (except for a few “well known” communities)

## Slide 14: BGP Updates: Withdrawn Routes
Used to “withdraw” network reachability
Each withdrawn route is composed of:
  Network Prefix
  Mask Length

## Slide 15: BGP Updates: Withdrawn Routes
AS 321
AS 123
192.168.10.0/30
192.192.25.0/24
.1
.2
x
Connectivity lost
BGP Update
Message
Withdraw Routes
192.192.25.0/24
Network Next-Hop Path
150.10.0.0/16 192.168.10.2 321 200
192.192.25.0/24 192.168.10.2 321

## Slide 16: BGP Routing Information Base
BGP RIB
D 10.1.2.0/24
D 160.10.1.0/24
D 160.10.3.0/24
R 153.22.0.0/16
S 192.1.1.0/24
Network Next-Hop Path
router bgp 100
network 160.10.1.0 255.255.255.0
network 160.10.3.0 255.255.255.0
no auto-summary
Route Table
*>i160.10.1.0/24 192.20.3.1 i
*>i160.10.3.0/24 192.20.3.1 i
BGP ‘network’ commands are normally used to populate the BGP RIB with routes from the Route Table

## Slide 17: BGP Routing Information Base
BGP RIB
router bgp 100
network 160.10.0.0 255.255.0.0
aggregate-address 160.10.0.0 255.255.0.0 summary-only
no auto-summary
Route Table
Network Next-Hop Path
D 10.1.2.0/24
D 160.10.1.0/24
D 160.10.3.0/24
R 153.22.0.0/16
S 192.1.1.0/24
*> 160.10.0.0/16 0.0.0.0 i
* i 192.20.3.1 i
s> 160.10.1.0/24 192.20.3.1 i
s> 160.10.3.0/24 192.20.3.1 i
BGP ‘aggregate-address’ commands may be used to install summary routes in the BGP RIB

## Slide 18: BGP Routing Information Base
BGP ‘redistribute’ commands can also be used to populate the BGP RIB with routes from the Route Table
BGP RIB
Network Next-Hop Path
router bgp 100
network 160.10.0.0 255.255.0.0
redistribute static route-map foo
no auto-summary
access-list 1 permit 192.1.0.0 0.0.0.255
route-map foo permit 10 match ip address 1
Route Table
D 10.1.2.0/24
D 160.10.1.0/24
D 160.10.3.0/24
R 153.22.0.0/16
S 192.1.1.0/24
*> 160.10.0.0/16 0.0.0.0 i
* i 192.20.3.1 i
s> 160.10.1.0/24 192.20.3.1 i
s> 160.10.3.0/24 192.20.3.1 i
*> 192.1.1.0/24 192.20.3.1 ?

## Slide 19: BGP Routing Information Base
BGP RIB
IN Process
Network Next-Hop Path
173.21.0.0/16 192.20.2.1 100
Update
* 173.21.0.0/16 192.20.2.1 100 i
BGP “in” process
  receives path information from peers
  results of BGP path selection placed in the BGP table
  “best path” flagged (denoted by “>”)
Update
Network Next-Hop Path
*>i160.10.1.0/24 192.20.3.1 i
*>i160.10.3.0/24 192.20.3.1 i
OUT Process
>

## Slide 20: BGP Routing Information Base
OUT Process
Network Next-Hop Path
160.10.1.0/24 192.20.3.1 200
160.10.3.0/24 192.20.3.1 200
173.21.0.0/16 192.20.2.1 200 100
BGP RIB
> 173.21.0.0/16 192.20.2.1 100
Network Next-Hop Path
*>i160.10.1.0/24 192.20.3.1 i
*>i160.10.3.0/24 192.20.3.1 i
*
IN Process
Update
Update
BGP “out” process
  builds update using info from RIB
  may modify update based on config
  Sends update to peers

## Slide 21: BGP Routing Information Base
BGP RIB
D 10.1.2.0/24
D 160.10.1.0/24
D 160.10.3.0/24
R 153.22.0.0/16
S 192.1.1.0/24
Network Next-Hop Path
*>i160.10.1.0/24 192.20.3.1 i
*>i160.10.3.0/24 192.20.3.1 i
*> 173.21.0.0/16 192.20.2.1 100
B 173.21.0.0/16
Route Table
Best paths installed in routing table if:
prefix and prefix length are unique
(not also in some other routing protocol)
Or if BGP has a lower “administrative
distance” than other protocol with the
same prefix/length

## Slide 22: An Example…
Learns about 35.0.0.0/8 from F and D
AS3561
B
E
C
D
F
A
AS200
AS101
AS21
AS675
35.0.0.0/8